## Slide 1: Construction Safety Monitoring System
Munesh Kumar – VGU6PB
Subject: Construction Information Technology Project
Instructor: Dr Arpad Barsi

## Slide 2: Project Overview
Safety Monitoring
Construction sites are among the most hazardous workplaces
High risk of accidents – safety and health of workers is critical
Key Features
Environmental Indicators:
Fire alarm
Temperature & humidity alarm
Laser security system (fall prevention from rooftops)
Danger Alerts:
Buzzer sound and blinking LED
Can be manually turned off via a push-button
Project Objective
Design a real-time safety monitoring system
System Components
Arduino Uno
Enhance on-site safety measures using smart technology
Sensor Kit (for monitoring environmental conditions)

## Slide 3: Sensors
1. Flame Sensor
2. Laser Emitter
3. Laser Resistor
4. Temperature and Humidity Sensor
5. LED
6. Button
7. Buzzer

## Slide 4: Operational principle
🔥 Flame Detection
  Flame sensor detects presence of fire
  Triggers: Buzzer + Green blinking LED
🛑 Rooftop Edge Perimeter Warning
  Laser emitter creates a safety perimeter
  If beam is interrupted, activates:
    Buzzer
    Red blinking LED
🌡️ Temperature Alert
  If temperature exceeds predefined limit:
    System triggers buzzer
    Blue blinking LED indicates overheating
💧 Humidity Alert
  When humidity crosses threshold:
    Same alerts as temperature system
    Buzzer + Blue blinking LED
🖲️ Manual Override Button
  Deactivates all alarms (buzzer + LEDs)
  Allows quick manual control in emergency or testing situations

## Slide 5
unsafe areas conditions
Fires risk
bad weather conditions

## Slide 6: Demonstration of flame detection
Aim: Detection of flame or open fire near on site
Here: representation by using a lighter as flame
In case of fire detection: Buzzer & LED activation (blinking green)

## Slide 7: Demonstration of laser perimeter system
Aim: Creating a virtual safety boundary on the roof by a laser beam
If someone crosses the entrance-detecter line, it signals that the worker is in a dangerous area by a buzzer and a Blue blinking LED
Utilization in reality: The OSHA-defined distance between the rooftop edge and working area is minimum 6 feet
  Laser perimeter system could be set up at that distance too

## Slide 8: Demonstration of temperature and humidity alert
Aim: Detection of abnormal temperature and humidity for proper working conditions
  The values have to be within OSHA-defined ranges: they can’t exceed 35 °C or 29 °C with 75% humidity.
If one or both limits are exceeded, the system triggers the buzzer and the LED that blinks Red.
Here: lower limits used for representation purpose
Aim of using different LED colors is to indicate which warning system singals

## Slide 9: Demonstration

## Slide 10: Conclusion
Construction Safety Monitoring System: minimizes the occurence of various safety risks on construction site.
Improves safety on construction sites.
Alerts workers to fires, unsafe areas, and bad weather conditions.
Effective solution for enhancing safety
  Further improvement possibilities: regular testing, calibration, personnal treaining

## Slide 11: Thank you for your attention!
Questions?
Munesh Kumar – VGU6PB
Mirna Makhlouf – X70AKT
Petra Hédl – SUX9GX
Construction Information Technology Project

## Slide 12: Code